## Slide 1
Simplified Use-Case of Graph Neural Networks (GNNs) for Predicting Synthetic Lattice Stability
Alexander Adams
Department of Mechanical Engineering and Materials Science, University of Pittsburgh, Pittsburgh, PA 15260
June 9th 2026
Notes: Predicting the Mechanical Properties of Complex Lattice Metamaterials Using Graph Neural Networks

## Slide 2
Overview
Predict stiffness of Voronoi lattice structures from graph topology using a Graph Convolutional Network (GCN), trained on 3,000 synthetic FEA simulations (Abaqus). Experiments span 8 phases of optimizer, representation, and objective improvements.
Progress Summary
Baseline: 2-layer GCN, Adam optimizer | Test R²: 0.9148
Phases 1-2: Optimizer comparison (AdamW, SGD) — Adam remains best
Phase 3: Weighted edges | Prediction-set R²: 0.3637 → 0.4336
Phase 4: Richer node features | Test R²: 0.9148 → 0.9403
Phase 5: Multi-seed validation | Confirms improvement is real
Phase 6: Graph-level summary features | Mean test R²: 0.9411
Phase 7-8: Target normalization | Best mean test R²: 0.9447

## Slide 3
Baseline Configuration
Model Architecture
2-layer GCN
Hidden dimension: 24
Node features: x, y coordinates
Optimizer: Adam
Weight decay: 1e-5
Training Schedule
Phase 1: lr = 0.003 for 200 epochs
Phase 2: lr = 0.0005 for 700 epochs
Baseline Metrics
0.8424
Val R²
0.9148
Test R²
0.003818
Test RMSE
0.003003
Test MAE

## Slide 4
Optimizer Comparison (Phases 1–2)
Phase 1: Initial Comparison (Flawed)
Tested AdamW, SGD + momentum, SGD + Nesterov
Issue: changed hidden_dim, regularization, schedule, and early stopping simultaneously
All optimizers performed much worse than baseline — results were not clean
Phase 2: Fair Optimizer Comparison
Optimizer | Test R² | Outcome
Adam (control) | 0.9148 | Best — matches baseline exactly
AdamW | 0.5101 | Substantially worse
SGD + Momentum | 0.1424 | Far below baseline
SGD + Nesterov | ~0.14 | Far below baseline

## Slide 5
Phase 3 (Weighted Edges)
Change
adjacency_area.csv used as weighted connectivity instead of binary edges only
edge_weight passed into both GCNConv layers
Observed Impact
Adam Test R²
0.9148
→
0.9113
Adam Pred-Set R²
0.3637
→
0.4336
AdamW Test R²
0.5101
→
0.5560
Interpretation: Weighted edges preserve real graph information and improve out-of-distribution behavior somewhat, but do not move the held-out test ceiling. Retained for all future runs.

## Slide 6
Phase 4: Richer Node Features
Node Features Added (derived from existing data at load time)
x, y coordinates (original)
Node degree
Weighted degree
Distance from specimen center
Boundary indicator
Mean incident edge length
Max incident edge length
Mean incident edge weight
Impact vs. Baseline
Val R²
0.8424 →
0.9386
Test R²
0.9148 →
0.9403
Test RMSE
0.003818 →
0.003197
Test MAE
0.003003 →
0.002448
Strongest single improvement. Confirmed stable across multiple seeds (mean test R²: 0.9380). Best prediction-set generalization baseline.

## Slide 7
Phase 5: Multi-Seed Validation
Purpose
Re-run the richer-feature Adam baseline across multiple random seeds to confirm the improvement is stable and not a lucky split.
Multi-Seed Results (Richer Node Features)
0.9414
Mean Val R²
0.9380
Mean Test R²
0.003086
Mean Test RMSE
0.4964
Mean Pred-Set R²
Test R² Range Across Seeds: 0.9339 to 0.9467
Best single-seed result (0.9403) was somewhat optimistic, as expected from variance
Multi-seed mean still clearly outperforms original baseline (0.9148 → 0.9380)
Held-out test split is stable across seeds; prediction set shows higher variance (out-of-distribution weakness)

## Slide 8
Phase 6: Graph-Level Summary Features
What Was Added
Node count, edge count, graph density
Total / mean / std edge weight
Degree mean / std
Weighted degree mean / std
Center-distance mean / std
Graph-level features are concatenated after pooling, before the output layer. All features normalized using training-split statistics.
Multi-Seed Results
Mean Val R²
0.9414 →
0.9410
Mean Test R²
0.9380 →
0.9411
Mean RMSE
0.003086 →
0.003003
Mean Pred-Set R²
0.4964 →
0.4035
Marginal improvement on held-out test; prediction-set R² declined. Graph features help in-distribution fit but do not yet resolve out-of-distribution robustness.

## Slide 9
Phases 7–8: Target Normalization
Approach
Combined all confirmed positive improvements (Adam schedule, weighted edges, richer node features, graph-level summary features) and added target normalization to test whether scaling the regression target improves robustness.
Multi-Seed Results (Target Normalized)
0.9416
Mean Val R²
0.9447
Mean Test R²
0.002908
Mean Test RMSE
0.4459
Mean Pred-Set R²
Test R² Range Across Seeds: 0.9384 to 0.9549
Best mean held-out test accuracy to date (0.9411 → 0.9447)
Prediction-set R² improved vs. graph-feature run (0.4035 → 0.4459), but still below richer-node-feature run (0.4964)
Tradeoff exists: best test accuracy = richer graph + target normalization; best pred-set generalization = richer node features only

## Slide 10
Phase By Phase Summary
Phase | Change | Mean Test R² | Mean Pred-Set R²
Baseline | 2-layer GCN, x/y features, Adam | 0.9148 | 0.3637
3 | Weighted edges | 0.9113 | 0.4336
4-5 | Richer node features (multi-seed) | 0.9380 | 0.4964
6 | + Graph-level summary features | 0.9411 | 0.4035
7-8 | + Target normalization (best test) | 0.9447 | 0.4459

## Slide 11
Current Assessment
1
Plain Adam with the two-phase schedule is the strongest training setup.
2
AdamW is consistently worse than Adam; SGD variants are not competitive.
3
Weighted edges are worth keeping — they preserve real graph structure.
4
Richer node features: largest single improvement; best prediction-set baseline (mean R² 0.4964).
5
Graph-level features + target normalization: best mean held-out test R² (0.9447) and RMSE (0.002908).
6
A measurable tradeoff now exists between in-distribution accuracy and prediction-set generalization.
7
Further gains are more likely from architecture or objective changes than from additional optimizer sweeps.

## Slide 12
Next Steps
What to Keep
Weighted edges enabled
Richer node features as the default representation baseline
Graph-level features + target normalization as the strongest test-accuracy config
Adam with two-phase schedule as the primary optimizer
Multi-seed repeats for all serious promotion decisions
What to Abandon
Broad SGD + momentum / Nesterov sweeps
AdamW as a primary focus (keep only as low-priority sanity check)
Architecture Directions to Explore
GIN
Graph Isomorphism Network — more expressive message passing
GraphSAGE
Inductive learning via neighborhood sampling
3-Layer Residual GCN
Deeper architecture with skip connections
Objective-Level: consider split strategy review and alternate target scaling if prediction-set mismatch appears structural.