## Slide 1
Graph Convolution Network (GCN) Voronoi Lattice Stiffness Optimization Progress Report
Alexander Adams
Department of Mechanical Engineering and Materials Science, University of Pittsburgh, Pittsburgh, PA 15260
June 30th 2026
Notes: Predicting the Mechanical Properties of Complex Lattice Metamaterials Using Graph Neural Networks

## Slide 2
Overview
Predict stiffness of Voronoi lattice structures from graph topology using a Graph Convolutional Network (GCN), trained on 3,000 synthetic FEA simulations (Abaqus). Experiments span 8 phases of optimizer, representation, and objective improvements.
Progress Summary
Baseline: 2-layer GCN, Adam optimizer | Test R²: 0.9148
Phases 1-2: Optimizer comparison (AdamW, SGD), Adam remains best
Phase 3: Weighted edges | Prediction-set R²: 0.3637 → 0.4336
Phase 4: Richer node features | Test R²: 0.9148 → 0.9403
Phase 5: Multi-seed validation | Confirms improvement is real
Phase 6: Graph-level summary features | Mean test R²: 0.9411
Phase 7-8: Target normalization | Best mean test R²: 0.9447

## Slide 3
Phase By Phase Summary
Phase | Change | Mean Test R² | Mean Pred-Set R²
Baseline | 2-layer GCN, x/y features, Adam | 0.9148 | 0.3637
3 | Weighted edges | 0.9113 | 0.4336
4-5 | Richer node features (multi-seed) | 0.9380 | 0.4964
6 | + Graph-level summary features | 0.9411 | 0.4035
7-8 | + Target normalization (best test) | 0.9447 | 0.4459

## Slide 4
Current Assessment
1
Plain Adam with the two-phase schedule is the strongest training setup.
2
AdamW is consistently worse than Adam; SGD variants are not competitive.
3
Weighted edges are worth keeping, they preserve real graph structure.
4
Richer node features: largest single improvement; best prediction-set baseline (mean R² 0.4964).
5
Graph-level features + target normalization: best mean held-out test R² (0.9447) and RMSE (0.002908).
6
A measurable tradeoff now exists between in-distribution accuracy and prediction-set generalization.
7
Further gains are more likely from architecture or objective changes than from additional optimizer sweeps.

## Slide 5
Next Steps
What to Keep
Weighted edges enabled
Richer node features as the default representation baseline
Graph-level features + target normalization as the strongest test-accuracy config
Adam with two-phase schedule as the primary optimizer
Multi-seed repeats for all serious promotion decisions
What to Abandon
Broad SGD + momentum / Nesterov sweeps
AdamW as a primary focus (keep only as low-priority sanity check)
Architecture Directions to Explore
GIN
Graph Isomorphism Network, more expressive message passing
GraphSAGE
Inductive learning via neighborhood sampling
3-Layer Residual GCN
Deeper architecture with skip connections
Objective-Level: consider split strategy review and alternate target scaling if prediction-set mismatch appears structural.