## Slide 1
Optimizing Material Strength Predictions in Complex Lattice Topologies Using Graph Neural Networks (GNNs)
Alexander Adamsa and Dr. Xing Liub
a Department of Mechanical Engineering and Materials Science, University of Pittsburgh, Pittsburgh, PA 15260
b Department of Mechanical and Industrial Engineering, New Jersey Institute of Technology, Newark, NJ 07102
June 2nd 2026

## Slide 2
Background
Stiffness-to-weight improvement over foams
Weight reduction possible with lattices
Critical industries relying on advanced architecture materials:
▸ Aerospace & Defense
▸ Energy Absorption
▸ Automotive Lightweighting
▸ Biomedical Implants
The Core Problem
Theory:
Lattices assumed to be perfectly periodic:
uniform strut dimensions, no defects,
identical unit cells throughout
Reality:
Manufacturing introduces defects: strut diameter variation, node misalignment, missing struts, surface roughness → Theoretical models fail to predict actual strength and fracture behavior → Shaikeea et al. (2022): KIc alone is INSUFFICIENT to characterize
fracture in 3D metamaterials
The global composites market was valued at approximately $110–133 billion in 2024, with projections to reach $205-313 billion by 2032–2034 (CAGR ~8–9%)
30-50%
$280B+
40%+
Advanced Materials Global Market (2024)

## Slide 3
Literature Review
Micropolar effects on elastic properties and fracture toughness of planar lattices
Micro-architectured materials: past, present and future
The toughness of mechanical metamaterials
Discrete asymptotic homogenization → explicit micropolar constitutive relations vs. relative density ρ̄
Hexagonal lattice internal length lᶜ ∝ ρ̄^0.5, bending-dominated architectures need micropolar enrichment
Resolves discrepancies between Chen et al. 1998 gradient theory and experimental data
Manufactured ~10M-cell octet-truss specimens via large-area projection microstereolithography
Kᴵᴶ depends on both a/ℓ and load triaxiality λ, KI alone is insufficient; T-stress governs failure
Fracture mechanism map (ρ̄/εᴼ vs. T̄) fully characterizes failure, plane-stress < plane-strain toughness (reversed!)
Establishes nodal connectivity Z as the key parameter: stretching-dominated (Z≥4) vs. bending-dominated (Z=3)
Fracture toughness Kᴵᴶ ∝ ρ̄ᵈ with d=2 (hexagonal), d=1 (triangular), d=0.5 (Kagome)
Kagome achieves density-independent toughness Gᴵᴶ, foundation for my topology exploration
Limitation: Computationally expensive with billions of DOF per simulation. Not scalable to defect-space exploration.
Limitation: Assumes perfect periodicity. Breaks down at higher relative densities and cannot handle defects.
Limitation: Cannot be applied off-the-shelf to discrete architected materials.
Fleck, Deshpande & Ashby, Proc. R. Soc. A (2010)
Berkache, Phani & Ganghoffer, Eur. J. Mech. A (2022)
Shaikeea, Cui, O'Masta, Zheng & Deshpande, Nat. Mater. (2022)
Notes: Berkache et al. (2022) used micropolar continuum theory to derive analytical scaling laws for hexagonal, triangular, and kagome lattices. Shaikeea et al. (2022): fracture in 3D octet-truss metamaterials depends on T-stress AND Kᴵ, not Kᴵ alone. Standard testing protocols developed for continua are fundamentally inadequate.
Fleck, Deshpande & Ashby (2010) show fracture toughness Kᴵᴶ ∝ ρ̄ᵈ via full lattice simulations.

## Slide 4
Research Workflow
Lattice
Geometry
Node positions,
connectivity,
boundary conds.
→
→
→
Tabular Features
Lattice geometry encoded into table for additional model training input
GNN Model
Graph-structured
forward pass;
learns stress fields
Predicted
Strength
Why Graph Neural Networks?
Lattice = graph: nodes are joints, edges are struts, GNNs operate natively on this representation
Inference is orders of magnitude faster than FE simulation (no billions of DOF solve)
Handles irregular, defective geometries that break analytical homogenization assumptions
Can encode graph topology as node/edge/global attributes

## Slide 5
Research Goals
4. Expected Outcome
3. Fracture Mechanism Prediction
1. Build The Graph Dataset
2. Train & Validate GNN
Generate diverse lattice geometries (hexagonal, kagome, triangular, octet-truss) with controlled randomness & defects. Run FE simulations to produce labeled strength outputs
Train on graphical lattice representations + tabular features. Validate Kᴵᴶ predictions against FE ground truth and Fleck/Berkache scaling laws
Extend model to predict failure mode (tensile fracture vs. elastic buckling) and the T-stress contribution, going beyond Kᴵᴶ-only characterization.
A fast and defect-aware model for lattice strength, enabling rapid design iterations without full FE solves. Potential to generalize across topologies.