## Slide 1
Voronoi Lattice Simulation Code Walkthrough and Pipeline Visualization
Alexander Adams
Department of Mechanical Engineering and Materials Science, University of Pittsburgh, Pittsburgh, PA 15260
June 9th 2026
Notes: Predicting the Mechanical Properties of Complex Lattice Metamaterials Using Graph Neural Networks

## Slide 2
0
User Parameters
Grid geometry: cell_size, n
Randomness sweep: 0.0 → 0.5 (3,000 sims)
Material: E = 2,000 MPa, ν = 0.30
Cross-section: rect_a × rect_b
Seed size = 0.30 mm
Displacement = 5.0 mm
1
Seed Point Generation
Hexagonal base grid (n × n)
Odd columns staggered ½ cell_height
Interior pts jittered ±randomness × cell_size
Edge pts fixed perpendicular (clean BCs)
Tag bottom / top / interior rows
Snap boundary rows to exact y values
2
Build Segments
For each seed: find neighbours within 2.5×cell_size
Sort by distance; cap at 12 candidates
Pick 3–6 connections randomly (stochastic)
Store via seg_key (canonical, deduplicated)
Produces structural variety per randomness level
3
Clean Geometry
Remove crossing beams (O(n²) while-loop)
Priority: remove non-boundary / longer beam
Thin side walls: keep prob = 0.45
Fix corner nodes (degree ≤ 1 → add connector)
Final deduplication via seg_key dict
4
Abaqus Model
Sketch beams as Lines → wire Part
Assign linear elastic material
Rectangular beam section (B21 elements)
Seed & mesh at 0.30 mm
Apply BCs: pin BL, roller bottom, disp top
Request S, U, RF, COORD, SF output
5
Submit FEA Job
mdb.Job() → submit(consistencyChecking=OFF)
waitForCompletion() blocks until done
nlgeom=OFF (linear static)
Single Abaqus increment (linear)
Outputs: job_name.odb
6
Post-Processing
node_features.csv — joint (x,y) coords
adjacency_area.csv — binary N×N adj. matrix
lattice_stiffness.csv — k = ΣRF₂ / δ (N/mm)
stress_matrix.csv — max S11 per beam (N×N)
Bounding-box prefilter for speed
7
Cleanup & Loop
Close ODB (release file handles)
Restore working directory (os.chdir)
Advance sim_idx → next randomness value
Repeat 3,000 times
Print ALL SIMULATIONS COMPLETE
↺ Next sim_idx (loop)
Pipeline Flowchart 2

## Slide 3
node_features.csv
N rows × 3 cols
GNN node feature matrix
node_id, x, y per joint
N varies per simulation
Spatial coords = primary node features
GNN loader must handle variable N
adjacency_area.csv
(N+1) × (N+1)
GNN edge connectivity
Binary symmetric matrix
Entry [i][j] = 1 if beam exists
Row/col headers are node_ids
Undirected graph representation
lattice_stiffness.csv
1 scalar value
Regression label
k = ΣRF₂ / displacement (N/mm)
Effective axial stiffness
Primary GNN prediction target
Varies with randomness & topology
stress_matrix.csv
(N+1) × (N+1)
Edge feature / aux label
Max |S11| per beam (axial stress)
Symmetric matrix like adjacency
Zero where no beam exists
Element assigned via bounding-box filter
Each of the 3,000 simulations produces its own folder randomness_XXXX/ containing these four files. GNN loaders must handle variable N (graph size varies per simulation).
Output Files 3