## Slide 1
GCN Voronoi Lattice Stiffness Optimization
Progress Report: Phases 9–18
Alexander Adams
Department of Mechanical Engineering and Materials Science, University of Pittsburgh, Pittsburgh, PA 15260
July 8th 2026

## Slide 2
Overview
Continue the GCN optimization study from Phase 9 through Phase 18, focusing on architecture comparisons, residual GCN stability, objective-function testing, and fixed-split ensembling.
Progress Summary
Phase 9: Architecture comparison | GCN-3 best single-seed Test R²: 0.9551
Phase 10: GCN-3 multi-seed validation | Mean Test R²: 0.9456
Phases 11–12: Residual GCN-3 | Best raw prediction-set mean R²: 0.5007
Phases 13–15: Residual retuning | Narrow LR retune improves stability; Mean Test R²: 0.9440
Phases 16–17: Huber loss | Tested for robustness, but not promoted
Phase 18: Fixed-split GCN-3 ensemble | Best held-out Test R²: 0.9555

## Slide 3
Phase 9: Architecture Comparison
Purpose
Compare architecture-level changes while keeping the current best positive pipeline fixed: Adam schedule, weighted edges, richer node features, graph-level summary features, and target normalization.
Single-Seed Architecture Results
Model | Test R² | Pred-Set R²
GCN-2 control | 0.9549 | 0.4011
GCN-3 | 0.9551 | 0.4497
GraphSAGE | 0.9538 | 0.3876
GIN | 0.9508 | 0.4386

## Slide 4
Phase 10: GCN-3 Multi-Seed Validation
Purpose
Validate whether the small single-seed GCN-3 gain over the 2-layer control is real across five random seeds.
Multi-Seed Results (Plain GCN-3)
0.9411
Mean Val R²
0.9456
Mean Test R²
0.002882
Mean Test RMSE
0.4453
Mean Pred-Set R²
GCN-3 beat GCN-2 on test R² in 4 of 5 seeds
Mean test R² improved by +0.00090 and mean RMSE improved by -0.000025. The gain is small but consistent enough to promote GCN-3 for best average held-out test accuracy. Prediction-set performance remained effectively flat.

## Slide 5
Phase 11: Residual GCN-3 Single-Run Test
What Was Added
Hidden-state skip connections added to the promoted 3-layer GCN
Adam two-phase schedule kept fixed
Weighted edges retained
Richer node features retained
Graph-level summary features retained
Target normalization retained
Residual depth cleared the 0.95 single-run test-R² threshold, but did not outperform the plain GCN-3 seed-42 reference.
Single-Run Results
Validation R²
Residual
0.9389
Test R²
Residual
0.9542
Test RMSE
Residual
0.002801
Pred-Set R²
Residual
0.4437

## Slide 6
Phase 12: Residual Multi-Seed Validation
Purpose
Test whether the residual GCN-3 improvement is stable across multiple random seeds, especially on the prediction set.
Multi-Seed Results (Residual GCN-3)
0.9412
Mean Val R²
0.9424
Mean Test R²
0.002964
Mean Test RMSE
0.5007
Mean Pred-Set R²
Plain GCN-3 Test R²: 0.9456 | Residual GCN-3 Test R²: 0.9424
Residual GCN-3 should not replace plain GCN-3 for mean test accuracy. However, it became the strongest prediction-set model tested so far, suggesting skip connections may help out-of-distribution behavior while introducing seed instability.

## Slide 7
Phases 13–15: Residual GCN-3 Retuning
Phase | Change | Test R² | Pred-Set R²
13 | Broad retune | 0.9541 single | 0.3545 single
14 | Narrow LR retune | 0.9537 single | 0.4600 single
15 | Narrow LR multi-seed | 0.9440 mean | 0.4724 mean
Result | Best residual compromise | Improved stability | Below plain GCN-3
Next | Stop broad retunes | Keep narrow LR candidate | Shift to evaluation

## Slide 8
Phases 16–17: Huber Loss Validation
Objective Change
Keep the narrow-LR residual GCN-3 setup fixed and replace MSE with Huber/SmoothL1 loss using beta = 0.75.
Multi-Seed Results (Residual Huber)
0.9410
Mean Val R²
0.9430
Mean Test R²
0.002953
Mean Test RMSE
0.4555
Mean Pred-Set R²
Huber worst-seed Test R² improved over original residual: 0.9257 → 0.9310
Huber helped tail stability somewhat, but still underperformed narrow-LR residual and plain GCN-3. It also reduced prediction-set performance, so the Huber branch should be de-prioritized.

## Slide 9
Phase 18: GCN-3 Fixed-Split Ensemble
Ensemble Strategy
Keep one shared train/validation/test split fixed using split seed 42. Train five plain GCN-3 members with model seeds 11, 42, 73, 101, and 202. Average predictions across validation, test, and prediction sets.
Fixed-Split Ensemble Results
0.9400
Validation R²
0.9555
Test R²
0.002759
Test RMSE
0.4369
Pred-Set R²
Best held-out test result achieved so far
The ensemble clearly exceeded the 0.95 test-R² target, but it is a fixed-split result, not a new multi-split mean benchmark. It improved in-distribution test accuracy, but did not improve prediction-set behavior.

## Slide 10
Phase 9–18 Summary
Phase | Change | Test R² | Pred-Set R²
9 | Architecture comparison | 0.9551 single | 0.4497
10 | GCN-3 multi-seed | 0.9456 mean | 0.4453
12 | Residual multi-seed | 0.9424 mean | 0.5007
15 | Narrow-LR residual | 0.9440 mean | 0.4724
18 | GCN-3 ensemble | 0.9555 fixed | 0.4369

## Slide 11
Current Assessment
1
Plain GCN-3 is now favored over GCN-2 for best average held-out test performance.
2
The benefit from extra depth is real but modest; it does not solve prediction-set robustness.
3
GIN and GraphSAGE did not provide a compelling improvement over the control pipeline.
4
Residual GCN-3 gives the best raw prediction-set mean, but is too unstable to promote.
5
Narrow-LR residual GCN-3 is the strongest stabilized residual compromise.
6
Huber loss improved tail stability slightly, but did not justify promotion.
7
Fixed-split GCN-3 ensembling is now the strongest held-out test result overall.

## Slide 12
Next Steps
What to Keep
Plain GCN-3 as promoted model
Adam two-phase schedule
Weighted edges and richer node features
Graph-level features + target normalization
Repeated seeds for promotion decisions
What to De-Prioritize
GIN and GraphSAGE
Broad residual retunes
Huber-loss branch
Additional optimizer sweeps
Highest-Value Directions
Error Analysis
Inspect errors by stiffness range, graph size, density, and weighted-degree statistics.
Distribution Shift
Compare train/test/prediction-set feature distributions to identify structural mismatch.
Inference Aggregation
Use plain GCN-3 ensembling when the goal is maximum fixed-split held-out accuracy.